PLUMBING & DRAINAGE STATUS REPORT

LOT NO:  …………………………..	ORIGINAL PERMIT NO: ………………………….

STREET / LOCATION: …………………………………………………………………………...……..

PLUMBING FILE SIGHTED	HOUSE TYPE

[  ] Yes   [  ] No	[  ] Highset	[  ] Low set	[  ] Units

INSPECTION RECORDS ON FILE	TYPE

[  ] Yes   [  ] No	[  ] Drains	[  ] Water Test	[  ] Final

DRAINAGE INSTALLATION AS PER PLAN ON FILE

[  ] Yes   [  ] No	[  ] Requires as constructed plan

SEWER DRAINAGE		DRAINAGE MATERIALS

[  ] Town sewer	[  ] Septic Tank	[  ] EW 	[  ] UPVC	[  ] Concrete	[  ] Other

NOTE: Bore separation

[  ] prior to 1982: 0 metres 	[  ] 1982: 50 m 	[  ] after 1983: 100 m

TANK OR ABSORPTION TRENCH

[  ] Existing	[  ] Replaced	Year replaced: …………………….

If replacement works carried out, inspection records available 	[  ] Yes	[  ] No

As constructed plans on file of replacement work: 	[  ] Yes	[  ] No

Does replacement trench comply with 100 m distance to bore	[  ] Yes	[  ] No

TYPE OF INVESTIGATION

[  ] Site visual inspection	[  ] Excavation	[  ] Camera	[  ] Plumbing file

COMMENTS: …………………….…………………….………………….………………………….

STACKWORK & WASTES	[  ] CI	[  ] Gal	[  ] UPVC	[  ] Other

VENT SIZE:    ………………..

COMMENTS: …………………….………………….…………………….………………………….

ASSESSMENT OF WATER SERVICE	[  ] Gal	[  ] Copper	[  ] PVC	[  ] Other

Specify

COMMENTS: …………………….…………………….…………………….……………………….

TEMPERING VALVE INSTALLED	[  ] Yes	[  ] No	Location ……………….

NOTE: Required to be installed after 3 April 1995.

VISUAL INSPECTION OF FIXTURES INSTALLED ON PROPERTY

WC	BSN	Bath	Trough	Shower	Shower over bath	Sink	Other

DT complies	[  ] Yes	[  ] No	ORG complies 	[  ] Yes	[  ] No

Up until 1983 DTs did not service primarily as ORGs and therefore height may vary in relation to internal FW grate levels and fixture overflow levels.

NOTE: Where this occurs, although not mandatory, consideration should be given to lowering the DT top to 100 mm below the lowest internal fixture grate to lessen the effect of any surcharge from the sewerage system, or install a reflux valve.

ORG height between 1983 and 1993 complies with 75 mm height difference.

ORG height from 1993 to be minimum 100 mm below inside FW/Fixture overflow level.

NOTE: 	In all installations the height of the grating will be at a suitable height to prevent infiltration of stormwater from the surrounding areas into the drainage system.

COMMENTS: …………………….………………….…………………….………………………….

…………………….………………….…………………….……………………….………………….

Have unapproved works been carried out? 		[  ] Yes	[  ] No

COMMENTS: …………………….………………….…………………….………………………….

…………………….………………….…………………….……………………….………………….

Plumbing and drainage work pertaining to the above permit [  ] appear to comply [  ] do not comply with existing plans and plumbing codes pertaining to the standards which applied at the time of construction, including works carried out after the Occupancy Permit was issued.

BUILDING PRACTITIONER

Name: ………………………………….……..	Registration No: …………..………………..

Signature: ……………………………..……..	Date:	……………………………..……..

NOTES:

…………………….…………………….…………………….……………………….………………….

…………………….…………………….…………………….……………………….………………….

…………………….…………………….…………………….……………………….………………….

…………………….…………………….…………………….……………………….………………….

…………………….…………………….…………………….……………………….………………….

…………………….…………………….…………………….……………………….………………….

…………………….…………………….…………………….……………………….………………….